True Blue

Bezos startup developing hydrocarbon engine for United Launch Alliance

to replace RD-180

Blue Origin is well along in development of the BE-4 liquid natural gas-fueled rocket engine, left, and has hot-fired its pre-burner and main injector assembly (above) at its BE-4 engine facility near Van Horn, Texas.

Frank Morring, Jr. Washington

U

nited Launch Alliance (ULA) and Blue Origin, the secretive Seattle-based space-vehicle company founded and funded by Amazon.com chief Jeff Bezos, believe they can complete development and start flying a 550,000-lb.-thrust rocket engine to replace the Russian-built RD-180 as the Atlas V power plant as early as 2017, without government money.

ULA will pay Blue Origin an unspecified but "significant" sum to help defray the cost of developing its BE-4 engine (see illustration), which has been in the works under wraps for the past three years near Seattle and at the Blue Origin test facility near Van Horn, Texas. The launch services company selected the BE-4 after kicking off a search for an RD-180 replacement when political tensions threatened continued supply of the big Russian engine.

"To develop a liquid rocket engine takes a solid seven years, sometimes longer," says Tory Bruno, ULA president and CEO. "Blue is already several years into that cycle. So by partnering with them we have the opportunity

to cut that cycle in half, which means that, say, about four years from now we would be in a position to begin flying rockets with this engine technology."

Developed for Blue Origin's planned human Orbital Vehicle, the BE-4 (designating the fourth Blue engine) is an oxygen-rich staged-combustion single-shaft rocket engine designed to burn liquefied natural gas.

"Liquefied natural gas is almost 100% methane; it has a few other hydrocarbons in it," says Bezos, who appeared with Bruno at a Washington press conference to announce the deal. "We're designing the engine to run on liquefied natural gas or methane. They're both roughly the same density, but methane is considerably more expensive because to remove the last little bit of other kinds of hydrocarbons is costly. Cost/operability is what drives us designing the engine."

Development has benefited from modern computer modeling techniques, additive manufacturing and other new approaches to design, the two executives say. Staged-combustion testing of the pre-burner and main injector assembly has been conducted (inset photo), and turbopump and main valve tests are in preparation. Full-scale testing of the BE-4 is scheduled to begin in 2016, according to Blue Origin.

Bezos has been using his own deep pockets to endow development of the new engine and everything else Blue Origin is doing, and he stressed that the engine-development effort is "fully funded" to avoid a costly "start-and-stop" workflow. The company plans to offer the BE-4 engine commercially once it is ready, and to make it reusable for eventual vertical-takeoff-and-land-ing operations with its own vehicle, drawing on the "self-cleaning" properties of liquefied hydrocarbon fuel to avoid soot and other by-products.

That application is in the future, however. Near-term plans call for "feathering" the BE-4 into the Atlas V vehicle set as needed.

"The BE-4 is not a one-for-one replacement for the RD-180, which is a kerosene-burning engine," says Bruno. "We intend to pair these in our baseline Atlas vehicle, and provide actually higher-performance, higher-thrust levels together than we have now. The RD-180 is a great engine; it is a real workhorse, it is high-performance, but this is an opportunity to really jump into the 21st century with modern technology so we can achieve more performance and a lower cost."

The two-bell RD-180, built by NPO Energomash, generates 860,000 Ib. thrust. The BE-4 thrust level is comparable to the AR-1 engine under development by Aerojet Rocketdyne (AJR) as a possible RD-180 replacement, which would also be twinned for the Atlas V application. AJR is responding to a U.S. Air Force request for information (RFI) on what it would take to replace the Russian engine by arguing that risk-reduction work done with NASA funding will dramatically cut the time to get a prototype of that engine—also a hydrocarbon-fueled oxygen-rich staged-combustion configuration—on the test stand (AW&STSept. 15, p. 27).

Bezos, who is said to spend one day a week at the Blue Origin engineering facility in Kent, Washington, says his company, too, has completed risk-reduction work on the BE-4. The company has finished developing and soon will flight-test the 110,000-lb.-thrust BE-3 liquid-hydrogen fueled engine, and may offer it for boost, upper-stage

and in-space applications.

The Air Force RFI plays into a groundswell of interest in Congress and at the Pentagon in developing an engine to replace the RD-180, which is frequently used to launch classified national security payloads on the Atlas V. In the fallout over Russia's annexation of the Crimean Peninsula, Russian officials have threatened to prohibit use of the engine for military purposes, raising concerns that worsening relations could ground crucial spacecraft. Bruno says his company's supply of the engines has been steady, and he expects it to continue. Despite movement in Congress that could make as much as $220 million available in the coming fiscal year toward an RD-180 replacement, ULA will continue to fund its separate development deal with Blue Origin, he says. However, the partnership would be open to using U.S. government funds to meet particular government needs. Bruno says he's getting positive feedback from stakeholders, and "those stakeholders include many members of Congress." ©

AVIATION WEEK & SPACE TECHNOLOGY/SEPTEMBER 22, 2014, (page 27)